## Slide 1: Shop Safety
Mr. Lidard’s Guide to Keeping All Your Body Parts

## Slide 2: Proper Attire
All students must…
  Wear closed-toed shoes.
  Must tie long hair behind their head.
Students may NOT…
  Wear loose clothing or jewelry.
  Wear headphones of any kind.
Students may…
  Wear an apron to protect clothing.
  Use gloves on certain equipment.

## Slide 3: Eye Safety
All students, teachers and visitors are required to wear safety glasses in the shop at all times, even if the equipment is not currently in use.
"All students, teachers, and visitors upon entering and participating in career and technology education or technology education laboratories, or visual arts classrooms and studios in the public schools, where the activities enumerated in the law are in progress, shall be required to wear, for general use, protective eye devices meeting the specifications of the American National Standard: Practice for Occupational and Educational Eye and Face Protection, Z87.1-1979 and OSHA Safety and Health Standard 29 CFR B'1910.133, both of which are incorporated by reference." (COMAR - Code of Maryland Regulations)

## Slide 4: The Safety Zone
The Safety Zone is a three dimensional space that exists at least two feet from each machine when that machine is “in use” and is not to be entered by any person except the operator and or the instructor. This space is designated to prevent injuries due to kick back, projectile debris, waste accumulation (slipping), out feed, and user interference. A good rule of thumb is that you should not be able to reach out and touch machinery that is being operated by another individual.
Do not talk to anyone while you or they are operating equipment.
Never stand on the right side of a Band Saw.

## Slide 5: Band Saw
Have all cut lines clearly marked and check all material for foreign objects before cutting.
Set the blade guide to 1/8" above the cutting surface to avoid twisting the blade as you work.
Allow the saw to reach full speed before cutting.
Keep your hands two inches from either side of the blade, holding the material firmly on the table. If you need to cut a smaller piece, use a push stick.
Do not force wood through the blade. When cutting a tight curve, make relief cuts, then push the wood slowly without twisting or bending the blade.
Use a V-block when cutting a round material, such as a dowel.
If you hear a clicking sound or if the blade breaks, turn off the saw and notify your instructor.
When backing out of a cut, turn the machine off first to avoid un-tracking the blade.
Turn off the Band Saw when finished cutting and wait for the blade to come to a complete stop before cleaning the area with a broom and dustpan.
Notes: Never stand on the left side of the table.

## Slide 6: Drill Press
Identify where you plan to place the hole and check all material for foreign objects before drilling. Center punch all holes to be drilled.
When changing the drill bit, use a Chuck Key. Be sure to replace the Chuck Key on the side of the machine when not in use.
Use clamps and/or portable vices to hold down the wood. If you are unsure about where to clamp the wood, see your teacher.
Do not drill into the table! Always have a scrap piece of wood between your work and the table, and adjust the depth drop and table height for your intended operation before starting the drill.
Raise and lower the chuck and drill bit using the feed wheel.
Let the bit do the work, and gently blow debris out of a hole to prevent friction or splitting.
If a piece of wood begins to spin, stop the machine before attempting to remove it from the drill bit.
When you are finished, turn off the Drill Press and wait for it to come to a complete stop. Then, clean up using a dustpan and broom.

## Slide 7: Scroll Saw
Have all cut lines clearly marked, and check the material for foreign objects before cutting.
Check the machine for broken or loose parts and adjust the blade guard so that it is 1/4 inch above the highest part of the wood.
Make sure the stock is placed firmly against the table, and never put your hands in line with the blade.
Start the machine at the lowest speed and increase to working speed. Decrease the speed to 0 when finished.
Never force your wood into the blade – let the machine do the work.
If the scrap from your project should get trapped between the blade and the throat, immediately power off the machine and clear the scrap using a long piece of scrap wood once the machine comes to a complete stop. Avoid using your hands.
Scroll Saw blades break easily. When this happens, immediately power off the machine and inform your instructor.
Avoid backing out of a cut. If there is no way to avoid it, turn off the machine, wait until the blade has completely stopped, and then carefully back out.
Turn off the Scroll Saw when finished cutting, and wait for it to come to a complete stop before cleaning it with a dustpan and broom.

## Slide 8: Disk & Belt Sander
Draw lines indicating what needs to be sanded, and check all material for foreign objects before sanding.
Hands and fingers must be kept as far away from the sander as possible.
Check the sandpaper to ensure it is not torn or clogged up.
The disk rotates in a counterclockwise direction which means that only the left portion of the disk should be used so that the rotation of the disk holds the work down on the table.
Use after the belt/disk sander is at full speed. Do not force the material, but rather, lightly push the material against the rotating disk.
Adjustments to the table should be made with the power off.
Wait for the Belt/Disk Sander to come to a complete stop before leaving. Then clean up all scraps using a dustpan and broom before leaving the machine.